| Project / BMP # |  | Date |  | Initials |
| --- | --- | --- | --- | --- |

VA DEQ DESIGN SPEC NO. 3:  GRASS CHANNELS

MINIMUM DESIGN CRITERIA:

- The Grass Channel must meet the following minimum design criteria. Spec No. 3 Sec 3

The bottom width must be between 4 and 8 feet.

The channel side slopes must be 3:1 or flatter.

The maximum contributing drainage area to any individual Grass Channel is 5 acres.

The longitudinal slope of the channel must be at least 1% and not greater than 4%.

The maximum flow velocity in the channel must be less than 1ft/s. during a 1-inch storm event.

The channel conveys must contain the 10-year design storm with at least 6 inches of freeboard and is non erosive.

PLAN REQUIREMENTS:

- Provide a site map identifying pertinent information regarding the Grass Channel

The contributing drainage area (CDA) boundaries, acreage, and land cover

Topography of the site area, including the Grass Channel

The locations of all conveyance system outfalls into the Grass Channel must be shown.

- Provide a plan view showing:

Overall Grass Channel grading

The layout and dimensions of the Grass Channel, including check dams

- Provide profiles, section views, and details that show the following:

Cross-section

Side slopes

Channel bottom width

Longitudinal slope

Check dam details

10-year storm elevation

COMPUTATIONS:

- Hydrologic analysis must be based on a 24-hour storm event using site specific rainfall precipitation frequency data recommended by the U.S. National Oceanic and Atmospheric Administration (NOAA) Atlas 14.

- The U.S. Department of Agriculture’s Natural Resources Conservation Service (NRCS) synthetic 24-hour rainfall distribution and models, including but not limited to TR-55 and TR-20; hydrologic and hydraulic methods developed by the U.S. Army Corps of Engineers;  or other standard hydrologic and hydraulic methods.

- The Rational Method may only be used for evaluating peak discharges.

- The Modified Rational Method may be used for evaluating volumetric flows to stormwater conveyances with a drainage areas of 200 acres or less.

- Provide pre- and post-development hydrologic, hydraulic, and routing information for the 1- year, 2- year, 10- year, and 100-year, 24-hour storms, as needed.

CHECK DAMS:

- Check dams, if used, must meet the following design criteria:  The items checked blow have not been properly addressed: Spec No. 3 Sec 6.4

Check dams must be composed of permanent, non-erodible material.

Check dams must be firmly anchored into the side slopes and channel bottom.

The maximum check dam height is 18 inches.

Armoring must be provided at the downstream toe of the check dam.

Check dams must be designed with a central weir.

The average ponding depth throughout the channel must be between 12 inches and 18 inches.

The ponded water at a downstream check dam cannot touch the toe of the upstream check dam.

Each check dam must have dewatering orifices to minimize standing water.

LANDSCAPING:

- The construction sequence must specify that a 6” layer of topsoil is required for all areas of the Grass Channel that will be stabilized with a permanent stand of vegetation.  The topsoil layer must be clearly shown on all basin related details to ensure that all post-construction elevations reflect the topsoil application.

- Landscaping of the basin slopes that requires mulching, spraying, etc. must be limited to areas above the elevation of the top of the principal outlet structure elevation and must be done in a manner that does not inhibit maintenance access.

MAINTENANCE:

- A Maintenance Agreement is required, identifying the person or organization responsible for maintenance, authorizing access for inspections and maintenance, and a providing a maintenance inspection checklist.

- Provide a summary of the long term maintenance requirements for the SWM facility on the SWM plan.

LOCATION:

- SWM facilities cannot be located within the public right-of-way limits.

- SWM facilities cannot be located within the 100’ RPA buffer or the SPA buffer unless an exception has been granted.

CONSTRUCTION:

- The sequence of construction must address the SWM facility installation and appropriate inspections, including:  initial site preparation, excavation/grading, and installation of the embankment, principal outlet structure, and emergency spillway.  We recommend the County staff be involved in these inspections.

- The sequence of construction must clearly state that a construction record drawing and certification that the stormwater management facility has been constructed in accordance with the approved plan must be submitted to the County and approved prior to Bond release.